## Slide 1: CVE-2021-22659
Prepared for: All Employees​
Prepared by: Nhat Dang & Trang Tran​
Release Date: 18/07/2024
For more information email nhat.fellowship@opswat.com & trang.fellowship@opswat.com
Graduate Fellowship Program

## Slide 2: AGENDA
Overview
CVE Analysis
Exploitation
Demo
Remediation

## Slide 3: OVERVIEW
CVE-2021-22659

## Slide 4
OVERVIEW
Description CVE-2021-22659
Rockwell Automation MicroLogix 1400 Version 21.6 and below may allow a remote unauthenticated attacker to send a specially crafted Modbus packet allowing the attacker to retrieve or modify random values in the register. If successfully exploited, this may lead to a buffer overflow resulting in a denial-of-service condition. The FAULT LED will flash RED and communications may be lost. Recovery from denial-of-service condition requires the fault to be cleared by the user.

## Slide 5
OVERVIEW
CVE-2021-22659
Vector: CVSS:3.1/AV:N/AC:L/PR:N/UI:N/S:U/C:L/I:L/A:H

## Slide 6: ANALYSIS
CVE-2021-22659

## Slide 7
PLC MicroLogix 1400
PLC MicroLogix 1400 is a type of Programmable Logic Controller (PLC) manufactured by Allen-Bradley, a prominent global PLC manufacturer.
MicroLogix 1400 provide three communications ports:
Channel 0: an isolated combination RS-232/ RS-485 communication port
Channel 1: Ethernet port
Channel 2: a non-isolated RS-232 communication port

## Slide 8
PLC MicroLogix 1400 communication.
Communication channels | Channel 0: isolated RS-232/RS-485 Channel 2: non-isolated RS-232 | Channel 1 : Ethernet
​ Protocol | DH-485 DF1 Full-duplex DF1 Half-duplex master and slave DF1 Radio modem Modbus RTU DNP3 ... | EtherNet/IP Modbus TCP/IP DNP3/IP

## Slide 9
Modbus protocol
Modbus protocol was developed in 1979 by Modicon (now part of Schneider) for industrial automation systems and Modicon programmable controllers.
Correlation between Modbus and OSI model
*Source: Modbus protocol Implement guide V1b

## Slide 10
Modbus protocol
Modbus operates on the "Client-Server (Master-Slave)" principle.
A Server can connect to one or multiple Client.
In Modbus protocol, there is no requirement for authentication between client and server.

## Slide 11
Modbus protocol
Function Code: tells the server what kind of action to perform.
Data: contains additional information that the server uses to take the action defined by the function code.
Message structure
*Source: Modbus protocol Implement guide V1b​

## Slide 12
Modbus TCP packet capture by Wireshark
Modbus TCP packet structure.

## Slide 13
Modbus protocol
Data type
Function Code

## Slide 14
Holding register

## Slide 15: EXPLOITATION
CVE-2021-22659

## Slide 16
Root Cause
Weak or absent authentication mechanism: Modbus TCP protocol lacks authentication requirements from the server (Modbus device) when receiving requests from clients (masters). This vulnerability makes the device susceptible to remote attacks without authentication.
Lack of Proper Input Validation and Math Overflow Risk: The device lacks robust input validation mechanisms for handling special Modbus packets, leading to security vulnerabilities such as buffer overflow and math overflow risks.
Absence of advanced security measures like encryption or TLS: Modbus TCP protocol does not integrate advanced security measures such as data encryption or TLS (Transport Layer Security) to protect data during transmission. This lack of security makes transmitted data vulnerable to theft or manipulation by attackers.

## Slide 17
In Modbus protocol, there is no requirement for authentication between Client and Server.
A unknow Client can send request without authentication.

## Slide 18
Modbus Poll application
Approach Modbus TCP packet ​

## Slide 19
Approach Modbus TCP packet
A ModbusTCP packet was send by Modbus Poll.

## Slide 20
​ Payload
Write payload send a ModbusTCP based on Modbus Poll packet.
Packet capture

## Slide 21
*Source: MicroLogix 1400 Programmable Controllers Bulletin 1766 /Math Instruction
Math Instruction on PLC Micro Logix 1400
Most math instructions use three parameters, Source A, Source B, and Destination
ADD of two registers

## Slide 22
​ Payload
Payload write random value into all register.

## Slide 23
​ Payload
Modbus packets were captured by Wireshark

## Slide 24
​ Result
Holding register before attacking
Holding register after attacking​

## Slide 25: DEMO
CVE-2021-22659

## Slide 26
Attacking

## Slide 28: REMEDIATION
CVE-2021-22659

## Slide 29
REMEDIATION
MetaDefender OT Security - provides full visibility into your OT assets and networks.
Detect CVE-2021-22659 on PLC Micrologix 1400 with MetaDefender OT Security

## Slide 30
REMEDIATION
Risk Mitigation & User Action All users, if applicable, may disable Modbus TCP support if it is not necessary for their MicroLogix 1400 implementation. Without Modbus TCP enabled, a potential attacker does not have access to exploit the device using this vulnerability.
Source: https://www.rockwellautomation.com/en-us/trust-center/security-advisories/advisory.PN1545.html

## Slide 31
References
MicroLogix 1400 Programmable Controllers (3/2024), Rockwellautomation Inc, https://literature.rockwellautomation.com/idc/groups/literature/documents/rm/1766-rm001_-en-p.pdf
Modbus Message Implement Guide V1 (2006) , Modbus Organization, https://modbus.org/docs
Modbus Application Protocol Specification (2006), Modbus Organization, https://modbus.org/docs
PN1545 Security Advisory, (2021), Rockwell Automation Inc, https://www.rockwellautomation.com/en-us/trust-center/security-advisories/advisory.PN1545.html%e2%80%8b.html

## Slide 32: THANK YOU
Prepared for: All Employees​
Prepared by: Nhat Dang & Trang Tran​
For more information email nhat.fellowship@opswat.com & trang.fellowship@opswat.com
Graduate Fellowship Program